## Slide 1: Gen2 Commands for PFS Engineering First Light
Shintaro Koshida

## Slide 2: Abstract
Requirement from PFS
AG and focusing command by Yoshida-san
How to develop Gen2 commands for Engineering first light
Action items

## Slide 3: Engineering items and required functions

## Slide 4: Process overview
Subaru related engineering process from Toward_EngineeringFirstLight_20200331
  P-6: AG camera validation
  P-7: POpt2 (WFC+PFI) alignment
  P-8: PFI-MCS relation
  P-9: TPA
  A-2: Spot measurement
For details, please see
  Toward_EngineeringFirstLight_20200331.xlsx
  PFS-GEN-IPM004017-03_FunctionList.pdf
    Details of each test items can refer from this document.
  PFS-GEN-IPM004000-01_commissioning_details.pdf

## Slide 5: Process overview: P-6 AG camera validation
This process contains 4 test items.
  Pixel scale and orientation
  Focusing
  Focal plane characterization
  Field acquisition, Guiding (Centroid and send error to the telescope)

## Slide 6: Process overview: P-6 AG camera validation
Pixel scale and Orientation measurement
Test process
  Slew the telescope to a field with many stars.
  Take a set of 6 AG camera images.
  Do astrometry and measure the pixel scale --- On-site analysis? Or analyze later?
  Put a slight offset on the telescope in R.A and Dec. direction individually.
  Take another set of AG camera images.
  Compare 2 images and check the orientation of the x/y direction. --- On-site analysis? Or analyze later?
  Rotate InR (60 deg) and repeat 1.—5.
Necessary functions … Subaru related functions are 2-1 and 2-2
  [ICS/PFI]
    AG to take image, do measurements and send results to the database and/or MHS
  [ICS/system]
    Gen2 commands to pointing the telescope to the field center
    Gen2 commands to move telescope slightly and take AG images, and rotate instrument rotator
  [Other Tools]
    Astrometry tool and analyzer to validate AG camera pixel scale and orientation

## Slide 7: Process overview: P-6 AG camera validation
Focusing
Test process
  Slew the telescope to a field (field acquisition) --- Perform focusing with auto-guide running ?
  Do focusing using AG
  Configure fibers and start AG
  Take SpS exposure scanning Hexapod z-position around the “on-focus” position
  Compare the spectra brightness to validate the AG on-focus position is equivalent to the on-focus position of the science fibers (i.e., the brightest position)
Necessary functions
  [ICS/PFI]
    AG process (AG actor?): take images, measure the centroid and send results to the database and MHS
    Run focusing software (Kawanomoto-san’s soft)
  [ICS/system]
    Gen2 commands to move Hexapod and rotate InR, and then make an exposure with AG camera (z? InR position at which focusing stars get into the camera FoV?)
    Gen2 commands to pointing the telescope to the field center
    Gen2 commands to change the focus position? (Launcher or OPE file)
  [Other tools]
    Focus position and parameter calculator
    Spectrum brightness estimator (Unless DRP has this function)
  [Fiber allocation]
    Fiber allocation software to check the transformation between the science focal plane and the AG focal plane.

## Slide 8: Process overview: P-6 AG camera validation
Focal plane characterization
Test process
  Slew the telescope to a given field.
  Calculate the focus position on “each” camera. Here, no focus adjustment is needed.
  Rotate the instrument rotator and calculate the focus position on each camera.
  Repeat item 3. w.r.t several InR position.
  Derive the planes which each AG camera travels and compare them.
Necessary functions
  [ICS/PFI]
    AG process to take images, calculate centroid and send the results to the database and MHS
  [ICS/system]
    Gen2 commands to pointing the telescope to the field center
    Focusing software (Kawanomoto-san’s? Or another method? )
    Gen2 commands to rotate InR and run focusing software
  [Other tools]
    Focus position and parameter calculator

## Slide 9: Process overview: P-6 AG camera validation
Field acquisition and guiding
Test process
  Slew the telescope to a field (field acquisition)
Necessary functions… Subaru related functions are 2-1 and 2-2
  [ICS/PFI]
    AG process to take images, calculate centroid and send the results to the database and MHS
    FITS header
  [ICS/System]
    Gen2 commands to pointing the telescope to the field center
    Guiding software to send image/error signal to the telescope
    Gen2 commands for field acquisition and tun on/off guiding

## Slide 10: Process overview: P-7 POpt2 alignment
This process contains 1 test item.
  WFC alignment
WFC alignment
Test process
  Slew the telescope to a field where we have a few stars on AG.
  Check focus, and defocus by shifting Hexapod-z ΔD5=0.5mm.
  Acquire the AG images.
  Measure Hexapod shift and tilt and apply correction.
  Repeat 3 and 4 a few times until shift and tilt meets the requirement.
  Repeat 2.—5. at a few EL angles.
Necessary functions
  [ICS/PFI]
    Run focusing software (Kawanomoto-san’s soft?)
    AG to take long exposure
  [ICS/system]
    Gen2 commands to pointing the telescope to the field center
    Gent2 commands to move telescope and Hexapod and then make exposures with AG camera
  [Other tools]
    Hexapod tilt/shift measurement software (Kawanomoto-san’s script)

## Slide 11: Process overview: P-8 PFI-MCS relation
This process contains 1 test item.
  Evaluate fiducial fiber position
Evaluate fiducial fiber position
Test process
  TBD
Necessary functions… Subaru related function is 2-1.
  [ICS/PFI+MCS]
    Sequence to take FF image, run centroid estimation and transform to F3C coordinate
  [ICS/system]
    Gent2 commands to illuminate FFs and measure their position
  [Other tools]
    Analyzer to FF positions on PFI with those measured at ASRD

## Slide 12: Process overview: P-9 TPA
This process contains 1 test item.
  Telescope pointing analysis
Telescope pointing analysis (Is this a Mitsubishi’s test item?)
Test Process
  Slew the telescope to set a given field.
  Take AG image.
  Calculate the Az/El offset.
    In the same way as the field acquisition is simpler
    Apply the derived offset and take another exposure to check. (TBC)
  Repeat step 1. 3. visiting every 30 deg of the azimuth and every 15 deg of elevation (from EL=30 75)
  Average the measured offsets.
  Update Az/El offset value of mount correction efficient, as the additional parameter (one of the Mitsubishi’s configuration files).
Necessary functions
  [ICS/PFI]
    Take AG images and run centroiding
  [ICS/system]
    Gen2 commands to pointing the telescope to the field center
    Guiding software to detect pointing error

## Slide 13: Process overview: A-2 Spot measurement
This process contains 1 test item.
  Take images for PSF characterization
Spot measurement
Test process
  TBD
Necessary functions
  [ICS/PFI+MCS]
    Move cobras to dedicated angles
  [ICS/SpS]
    BIA on/off
    Image acquisition
  [ICS/system]
    Gen2 command from cobra move to take image, moving telescope
  [DRP]
    Quick analysis system

## Slide 14: Process overview: A-2 Spectra Acquisition
This process contains 1 test item.
  Take images for PSF characterization
Spot measurement
Test Process
  Assumption: We dont take object spectra intentionally, having Cobra at given (theta, phi) positions.
  Move telescope (EL, InR) without Field Acquisition or Auto Guide
  Take SpS exposures
Necessary functions
  [ICS/PFI+MCS]
    Move Cobras to dedicated angles
  [ICS/SpS]
    BIA on/off
    Take image
  [ICS/system]
    Gen2 command from cobra move to take image, moving telescope
  [DRP]
    Quick analyser?

## Slide 15: Functions to be developed
In summary, the functions to be developed are as listed below.
  [ICS/PFI]
    AG process (AG actor?): take images, measure the centroid and send results to the database and MHS
    Run AG focusing software (Kawanomoto-san’s soft accommodated in AG actor)
    Sequence to take FF image, run centroid estimation and transform to F3C coordinate
  [ICS/PFI+MCS]
    Move cobras to dedicated angles
  [ICS/SpS]
    BIA on/off
    Image acquisition
  [ICS/system]
    Gen2 commands to move Hexapod and rotate InR, and then make an exposure with AG camera (z? InR position at which focusing stars get into the camera FoV?)
    Gen2 commands to pointing the telescope to the field center
    Gen2 commands to change the focus position? (Launcher or OPE file)
    Focusing software (Kawanomoto-san’s? Or another method? )
    Gen2 commands to rotate InR
    Guiding software to send image/error signal to the telescope
    Gen2 commands for field acquisition and tun on/off guiding
    Gen2 commands to move telescope slightly and take AG images, and rotate instrument rotator
    Gent2 commands to illuminate FFs and measure their position
    Gen2 command from cobra move to take image, moving telescope
  [Other tools]
    Focus position and parameter calculator
    Spectrum brightness estimator (Unless DRP has this function)
    Astrometry tool and analyzer to validate AG camera pixel scale and orientation
    Hexapod tilt/shift measurement software (Kawanomoto-san’s script)
    Analyzer to FF positions on PFI with those measured at ASRD
  [Fiber allocation]
    Fiber allocation software to check the transformation between the science focal plane and the AG focal plane.
  [DRP]
    Quick analysis system

## Slide 16: Functions to be developed
Those functions could be broken down into more elemental command blocks to realize the designed function in the previous page.
  Telescope/POpt2
    Slew the telescope
    Hexapod position setting
  PFI
    InR position setting
  AG
    AG camera exposure
    Focusing sequence
    AG position analysis
    Communication to telescope over AG position and error
    AG sequence control (AG on/off)
  MCS
    MCS exposure
    Fiducial fiber position analysis
    Cobra position setting
  SpS
    Fiducial fiber illumination
    Spectrograph exposure
    Turn on the calibration lamp on SpS

## Slide 17: Functions to be developed
Those functions could be broken down into more elemental command blocks to realize the designed function in the previous page.
Subsystem | Functions | Related Actors | Command name | Function ID | Memo
System | Slew the telescope (positioning, set offset, database/RADec/AzEl mode) |  | SetupField.sk, | 1 | 
Tel/POpt2 | Hexapod position setting |  | PFS_POPT2_MOVE2.sk (or M2setup.sk) | 2 | 
 | InR position setting |  | SetRotator.sk | 3 | 
PFI AG | Turn on/off the calibration lamp | PFI (TBC) | PFS_SPS_EXPOSURE.sk | 10 | Operation of lamp and exposure are done by this command.
AG | AG camera exposure | AGCC Actor | Agexp.sk | 4 | 
 | Focusing sequence | IIC (+AG?) | PFS_FocusAg.sk | 5 | 
 | AG exposure, position and centroid analysis, error report | AG (field ack) | PFS_StartAg.sk | 6 | 
 | Communication to telescope over AG position and error | AG |  |  | 
 | AG sequence control | AG |  |  | 
 | AG off/on | AG | Agon.sk, Agoff.sk, Agreconf.sk | 7 | Launcher?
MCS | MCS exposure | IIC | PFS_MCS_MULTI_EXP.sk | 8 | 
 | Fiducial fiber position analysis | IIC |  |  | 
 | Cobra position setting | IIC |  |  | 
SpS | Fiber illumination |  | PFS_FIBRE_LIGHT.sk | 9 | 
 | Take exposure | IIC | PFS_SPS_EXPOSURE.sk | 10 | 
 | Resolution selection | SpS or IIC |  |  | 
Fiber allocation |  |  |  |  | 
DRP |  |  |  |  | 
Others |  |  |  |  | 

## Slide 18: Other possible necessary commands
Get information of the registered information of a target from targetDB (for displaying, )
Automation of the core analysis software in the hexapod position analysis(“Test Process (WFC alignment) [Ref. 1]”).
Fiber configuration
An option for AGFOCUS not to adjust the focus in the end --- completed
AG actor FOCUS command: output the computed tilt of the focal plane… or focus position of each AG camera

## Slide 19: Command design for each required function

## Slide 20: Basic strategy of Gen2 command design for PFS
The basic sequencing of process in PFS side will be taken by “Actors” in most of the cases.
  Each skeleton files could be designed as a kind of a trigger to start procedures in PFS Actors.
  Interactions with Gen2
    Triggering the sequential process of Actors
    Telescope status management (MLP)
    Telescope control (Az, El, InsRot, Hexapod (including focus), etc…)
    Image transfer
For engineering purpose, there might be some occasions of additional interaction with Gen2 which would not be happening in the normal operation
  Hexapod adjustment

## Slide 21: Function ID 1: SetupField.sk
Slew telescope to the registered field center position. If RA and Dec is set to the current position or arbitrary Az and El, the field information will be optionally registered to opDB.
The current HSC command SetupField.sk can be used as a base structure.
  gen2@g2s2:/gen2/share/Git/kansoku/HSC/sk/IMAG/SETUPFIELD.sk
Required Functions:
  Slew telescope to a center of a field of interest
    Case1: Slew the telescope to arbitrary Az. and El.
    Case2: Pointing a certain target in opDB
  Collect the header information?
Communications to the other system
  Input to Gen2
    R.A. and Dec. of a field center (case2)
  Output
    R.A. and Dec. corresponding to actual telescope position (case1)
Header
  OBE_ID=PFS
  OBE_mode=ENG
  COMMAND=SETUPFIELD
  Script_Version=1.0
  Script_Author=PFS
  Script Update=2021/??/??
Default parameters
  DATASET_ID=DS000
  RA=!STATS.RA
  DEC=!STATS.DEC
  EQUINOX=!STATS.EQUINOX
  INSROT_PA=!TSCL.INSROTPA_PF
  OFFSET_RA=0
  OFFSET_DEC=0
  OBJECT=DUMMY
  Z=!TSCL.Z
  FILTER=NOP
  DBOBJECT=DUMMY
TBC
  Does the parameter such as OBJEECT or DBOBJECT to somewhere?
  Check how to register new field to opDB
  How to specify the parameter for InsRot? Maybe unlike Insrot_PA for HSC, because the rotation angle will be decided with the fiber configuration.

## Slide 22: Function ID 1: SetupField.sk
<Header>
OBE_ID=HSC
OBE_mode=IMAG
COMMAND=SETUPFIELD
Script_Version=0.3
Script_Author=Nakata/Tait/Utsumi
### This script is created based on SETUPFILED.sk of SupCam.
Script_Update=2013.02.02
Script_Update=2014.07.04
# Dispatcher_Version=1.0
# ESTIMATE=180
</Header>
<Default_Parameter>
DATASET_ID=DS000
RA=!STATS.RA
DEC=!STATS.DEC
EQUINOX=!STATS.EQUINOX
INSROT_PA=!TSCL.INSROTPA_PF
OFFSET_RA=0
OFFSET_DEC=0
OBJECT=DUMMY
Z=!TSCL.Z
FILTER=NOP
FILE=NOP
</Default_Parameter>
<Command>
:START
:MAIN_START
{
#
# AG off
#
EXEC TSC AG_TRACKING MOTOR=OFF ;
*Set INFO3="Target : $OBJECT"
Exec OBS Set_Message Instrument_Name=HSC ObsInfo1="SetupField : No Guiding / No Dithering" ObsInfo2=Clear ObsInfo3=$INFO3 ObsInfo4=Clear ObsInfo5=Clear ,
#
# calculate pointing
#
*IF "$FILE" == "NOP"
EXEC OBS CONVSECRADEC RASEC=$OFFSET_RA DECSEC=$OFFSET_DEC RABASE=$RA DECBASE=$DEC ;
EXEC OBS CALC_RADEC MODE=PLUS RABASE=$RA DECBASE=$DEC RAOFFSET=!STATOBS.RARELOUT DECOFFSET=!STATOBS.DECRELOUT ;
EXEC TSC INSROT_PF TELESCOPE=LINK COORD=ABS POSITION=$INSROT_PA ;
EXEC TSC TELDRIVE COORD=ABS RA=!STATOBS.RACALCOUT DEC=!STATOBS.DECCALCOUT EQUINOX=$EQUINOX ,
Exec OBS Set_Message Instrument_Name=HSC ObsInfo2="Slewing Telescope" ,
*ELSE
EXEC TSC INSROT_PF TELESCOPE=LINK COORD=ABS POSITION=$INSROT_PA ;
Exec OBS Set_Message Instrument_Name=HSC ObsInfo2="Slewing Telescope" ObsInfo4="Non Sidereal Tracking" ,
EXEC TSC TELDRIVE COORD=FILE TARGET=$FILE DIRECTION=TSC ;
EXEC OBS CONVSECRADEC RASEC=$OFFSET_RA DECSEC=$OFFSET_DEC RABASE=!STATS.RA DECBASE=!STATS.DEC ;
Exec TSC TELDRIVE_Offset COORD=ABS RA=!STATOBS.RARELOUT DEC=!STATOBS.DECRELOUT ;
*ENDIF
Exec TSC TelFocus Motor=on Coord=TSC F_Select=P_OPT2 Z=$Z ;
};
#
# chceck status
#
Exec OBS Set_Message Instrument_Name=HSC ObsInfo2="Waiting for Rotator/Focus/WindScreen to Settle" ,
Exec OBS Check_Status Mode=AND Timeout=0360 N1=[STATS.ROTDIF_PF -0.005 +0.005] ;
Exec OBS Check_Status Mode=AND Timeout=0030 N1=[STATL.ZDIF -0.005 0.005] ;
# Exec OBS Check_Status Mode=AND Timeout=0720 N1=[STATL.WINDSDIF -10.0 +0.5] ;
Exec OBS Check_Status Mode=AND Timeout=0720 N1=[STATL.WINDSDIF_SIGN -0.5 +10.0] ;
Exec OBS Set_Message Instrument_Name=HSC ObsInfo2="Done" ;
#
:MAIN_END
:END
</Command>

## Slide 23: Function ID 1: SetupField.sk
Operational sequence
  [Gen2] Display a message to Gen2 window saying “M2 Setup starting” (EXEC OBS SET_MESSAGE)
  [TSC] Send M2_SETUP command to TSC with parameters.
    If “FOCI” is set to “NOP”, the explicitly specified values for each axes are used. Otherwise, TSC will set the Hexapod position to PFS nominal position.
  [Gen2] Display a message to Gen2 window saying “M2 Setup done” (EXEC OBS SET_MESSAGE)

## Slide 24: Function ID 2: PFS_POPT2_MOVE2.sk
Header
  SCRIPT_AUTHOR=Moritani
  SCRIPT_UPDATE=2018.10.19
  OBE_ID=PFS
  OBE_MODE=SPEC_ENG
Default parameters
  SSYS=POPT2
  COMP=NONE
  X=!TSCV.PF_OFF_X
  Y=!TSCV.PF_OFF_Y
  Z=!TSCV.PF_OFF_Z
  TX=!TSCV.PF_OFF_TX
  TY=!TSCV.PF_OFF_TY
  (Below are for ADC mode)
  MMODE=MM
  EL=@status
  E0=0.0027
  E1=12.6755
  E2=-0.0992
  E3=0.2141
  E4=-0.0901
TBD
  The nominal position for PFI should be stored in TSC. It is called when “FOCI” is set to “PFS”
#**********************************************************************
#
# POpt2 Movement (Hexapod or ADC)
#
#**********************************************************************
:Header
SCRIPT_AUTHOR=Moritani
SCRIPT_UPDATE=2018.10.19
OBE_ID=PFS
OBE_MODE=SPEC_ENG
:Parameter
# for PFS
SSYS=POPT2
# component to move (HEXAPOD or ADC)
COMP=NONE
# Hexapod movement
X=!TSCV.PF_OFF_X
Y=!TSCV.PF_OFF_Y
Z=!TSCV.PF_OFF_Z
TX=!TSCV.PF_OFF_TX
TY=!TSCV.PF_OFF_TY
# ADC movement
## movement select by El. (EL) or Position in mm (MM)
MMODE=MM
## Elevation
EL=@status
## Coefficients of ADC position
E0=0.0027
E1=12.6755
E2=-0.0992
E3=0.2141
E4=-0.0901
## Input position
POSIN=!STATL.ADCPF_POS
:Command
:start
from "math" import pow
:main_start
*IF "$COMP" == "HEXAPOD"
EXEC TSC TUDRIVE MOTOR=ON X=$X Y=$Y Z=$Z TX=$TX TY=$TY;
*ENDIF

## Slide 25: Function ID 2: PFS_POPT2_MOVE2.sk
Operational sequence
  [Gen2] Display a message to Gen2 window
    “M2 Setup starting” (EXEC OBS SET_MESSAGE)
  [TSC] Send M2_SETUP command to TSC with parameters.
    If “FOCI” is set to “NOP”, the explicitly specified values for each axes are used. Otherwise, TSC will set the Hexapod position to PFS nominal position.
    Input parameters: FOCI, X, Y, Z, TX, TY, TZ
    Return value: None
  [Gen2] Display a message to Gen2 window
    “M2 Setup done” (EXEC OBS SET_MESSAGE)
Discussion
  Any necessity to record some parameters to database?
    Is the M2 position recorded into FITS header?
*IF "$COMP" == "ADC"
*IF "$MMODE" == "EL"
*SET ZA = (90-$EL)
# Calc. tan(za) calling dedicated DD command
#EXEC OBS CALC TAN_ARG=$ZA ;
#*SET TZA = !STATOBS.TAN
#*SET POSITION = ($E0 + $E1*$TZA + $E2*$TZA*$TZA + $E3*$TZA*$TZA*$TZA + $E4*$TZA*$TZA*$TZA*$TZA )
#EXEC OBS Set_message obsinfo3="ADC Position is $POSITION";
# Calc. tan(za) inside Abstract command
asn tza = tan($ZA)
asn pos = $E0 + $E1*@tza + $E2*@pow(@tza,2) + $E3*@pow(@tza,3) + $E4*@pow(@tza,4)
#EXEC OBS Set_message obsinfo1=clear obsinfo2=clear obsinfo3="ADC Position is @pos" obsinfo4=clear obsinfo5=clear;
#*ENDIF
*ELIF "$MMODE" == "MM"
#*SET POSITION = ($POSIN)
asn pos = ($POSIN)
*ELSE
#*SET POSITION = (!STATL.ADCPF_POS)
asn pos = (!STATL.ADCPF_POS)
*ENDIF
if (@pos) < (0)
asn pos = 0
endif
if (@pos) > (22)
asn pos = 22
endif
asn pos_char = "@pos"
EXEC OBS Set_message obsinfo1=clear obsinfo2=clear obsinfo3="ADC Position is @pos_char" obsinfo4=clear obsinfo5=clear,
#EXEC TSC ADC_PF MOTOR=ON F_SELECT=P_OPT2 COORD=abs POSITION=$POSITION ;
# EXEC TSC ADC_PF MOTOR=ON F_SELECT=P_OPT2 COORD=abs POSITION=@pos+1 TELESCOPE=Free ;
# EXEC OBS SLEEP SLEEP_TIME=1 ;
#EXEC TSC ADC_PF MOTOR=ON F_SELECT=P_OPT2 COORD=abs POSITION=@pos TELESCOPE=Free ;
if ((!STATL.ADCPF_POS - @pos) * (!STATL.ADCPF_POS - @pos)) > 0.01
EXEC TSC ADC_PF MOTOR=ON F_SELECT=P_OPT2 COORD=abs POSITION=@pos TELESCOPE=Free ;
endif
#wait for ADC to finish moving
asn posu= (@pos + 0.01)
asn posl= (@pos - 0.01)
Exec OBS CHECK_STATUS MODE=AND TIMEOUT=90 N1=[STATL.ADCPF_POS @posl @posu] ;
*ENDIF
:main_end
:end

## Slide 26: Function ID 2: M2_SETUP.sk
The current common command M2_setup.sk can be used with no or very little modification.
  gen2@g2s2:/gen2/share/Git/kansoku/COMMON/sk/LAUNCHER/M2_SETUP.sk
Header
  OBE_ID=PFS
  OBE_MODE=ENG
  COMMAND=M2_SETUP
  SCRIPT_ID=M2_SETUP.sk
  Script_Version=1.0
  Script_Author=PFS
  Script Update=2021/??/??
Default parameters
  FOCI=nop
  X=nop
  Y=nop
  Z=nop
  TX=nop
  TY=nop
  TZ=nop
TBD
  The nominal position for PFI should be stored in TSC. It is called when “FOCI” is set to “PFS”
<Header>
OBE_ID=COMMON
OBE_MODE=LAUNCHER
COMMAND=M2_SETUP
SCRIPT_ID=COMMON
Script_Version=1.0
Script_Author=ocs
Script_Update=2010/09/09
Dispatcher_Version=2.0
</Header>
<Default_Parameter>
FOCI=nop
X=nop
Y=nop
Z=nop
TX=nop
TY=nop
TZ=nop
</Default_Parameter>
<Command>
:START
:MAIN_START
exec obs set_message instrument_name=!FITS.SBR.MAINOBCP obsinfo1="M2 Setup starting..." obsinfo2=clear obsinfo3="x=!TSCV.PF_OFF_X y=!TSCV.PF_OFF_Y z=!TSCV.PF_OFF_Z tx=!TSCV.PF_OFF_TX ty=!TSCV.PF_OFF_TY tz=!TSCV.PF_OFF_TZ" obsinfo4=clear obsinfo5=clear;
*IF "$FOCI" == "NOP"
Exec TSC M2_SETUP X=$X Y=$Y Z=$Z TX=$TX TY=$TY TZ=$TZ ;
*ELSE
Exec TSC M2_SETUP Foci=$FOCI ;
*ENDIF
exec obs set_message instrument_name=!FITS.SBR.MAINOBCP obsinfo1="M2 Setup done" obsinfo4="x=!TSCV.PF_OFF_X y=!TSCV.PF_OFF_Y z=!TSCV.PF_OFF_Z tx=!TSCV.PF_OFF_TX ty=!TSCV.PF_OFF_TY tz=!TSCV.PF_OFF_TZ";
:MAIN_END
:END
</Command>

## Slide 27: Function ID 2: M2_SETUP.sk
Operational sequence
  [Gen2] Display a message to Gen2 window
    “M2 Setup starting” (EXEC OBS SET_MESSAGE)
  [TSC] Send M2_SETUP command to TSC with parameters.
    If “FOCI” is set to “NOP”, the explicitly specified values for each axes are used. Otherwise, TSC will set the Hexapod position to PFS nominal position.
    Input parameters: FOCI, X, Y, Z, TX, TY, TZ
    Return value: None
  [Gen2] Display a message to Gen2 window
    “M2 Setup done” (EXEC OBS SET_MESSAGE)
Discussion
  Any necessity to record some parameters to database?
    Is the M2 position recorded into FITS header?

## Slide 28: Function ID 3: SetRotator.sk
The rotator setting command can be operated directly from gen2.
  PFS might be able to get status from Gen2 anyway
Header
  OBE_ID=COMMON
  OBE_MODE=TOOL
  COMMAND=SetRotator
  Script_ID=COMMON01
  Script_Version=1.0
  Script_Author=George
  Script_Update=2000/11/28
  Dispatcher_Version=2.0
  ESTIMATE=($NFRAME*$NSTEP*4.0+$NSTEP*10.0+20.0+150.0)
Default parameters
  F_SELECT=!STATL.TSC_F_SELECT
    *F_SELECT=!STATL.TSC_F_SELECT,CS_Opt,CS_IR,NS_Opt,NS_IR,P_Opt,P_Opt2,P_IR
  INSROT_PA=nop
  TELESCOPE=LINK
    *TELESCOPE=LINK,FREE
  OBSERVATION_ID=nop
  DATASET_ID=nop
  SPIKE_ID=nop
Note
  The nominal position for PFI should be stored in TSC. It is called when “FOCI” is set to “PFS”
<Header>
OBE_ID=COMMON
OBE_MODE=TOOL
COMMAND=SetRotator
Script_ID=COMMON01
Script_Version=1.0
Script_Author=George
Script_Update=2000/11/28
Dispatcher_Version=2.0
ESTIMATE=($NFRAME*$NSTEP*4.0+$NSTEP*10.0+20.0+150.0)
</Header>
<Default_Parameter>
F_SELECT=!STATL.TSC_F_SELECT
*F_SELECT=!STATL.TSC_F_SELECT,CS_Opt,CS_IR,NS_Opt,NS_IR,P_Opt,P_Opt2,P_IR
INSROT_PA=nop
TELESCOPE=LINK
*TELESCOPE=LINK,FREE
OBSERVATION_ID=nop
DATASET_ID=nop
SPIKE_ID=nop
</Default_Parameter>
<Command>
:START
:MAIN_START
*IF "$F_SELECT" == "P_IR"
Exec TSC InsRot_PF Motor=ON TELESCOPE=$TELESCOPE Coord=ABS POSITION=$INSROT_PA ;
*ENDIF
*IF "$F_SELECT" == "P_OPT"
Exec TSC InsRot_PF Motor=ON TELESCOPE=$TELESCOPE Coord=ABS POSITION=$INSROT_PA ;
*ENDIF
*IF "$F_SELECT" == "P_OPT2"
Exec TSC InsRot_PF Motor=ON TELESCOPE=$TELESCOPE Coord=ABS POSITION=$INSROT_PA ;
*ENDIF
*IF "$F_SELECT" == "NS_OPT"
Exec TSC ImgRot Motor=ON TELESCOPE=$TELESCOPE Coord=ABS POSITION=$INSROT_PA ;
*ENDIF
*IF "$F_SELECT" == "NS_IR"
Exec TSC ImgRot Motor=ON TELESCOPE=$TELESCOPE Coord=ABS POSITION=$INSROT_PA ;
*ENDIF

## Slide 29: Function ID 3: SetRotator.sk
The instrument rotator will be operated frequently by various Gen2 commands so that it will be convenient to realize this function as a dd command.
EXEC TSC INSROT_PF TELESCOPE=LINK COORD=ABS POSITION=$INSROT_PA ;
Operational sequence
  [Gen2]
*IF "$F_SELECT" == "CS_IR"
Exec TSC InsRot Motor=ON TELESCOPE=$TELESCOPE Coord=ABS POSITION=$INSROT_PA ;
*ENDIF
*IF "$F_SELECT" == "CS_OPT"
Exec TSC InsRot Motor=ON TELESCOPE=$TELESCOPE Coord=ABS POSITION=$INSROT_PA ;
*ENDIF
*IF "$F_SELECT" == "CS"
Exec TSC InsRot Motor=ON TELESCOPE=$TELESCOPE Coord=ABS POSITION=$INSROT_PA ;
*ENDIF
:MAIN_END
:END
</Command>

## Slide 30: Function ID 4: AGEXP.sk
Make exposure of 6 AG cameras
Functions:
  Take simple exposures of AG cameras without operating telescope or other subsystems, and then save the image.
Header
  SCRIPT_AUTHOR=Moritani, Koshida
  SCRIPT_UPDATE=2021.10.05
  OBE_ID=PFS
  OBE_MODE=SPEC_ENG
Default parameters
  SSYS=PFI
  NFRAME=1
  EXPTIME=1
  OBJECT="test" # dark|test|object
  PFIVISITID=0 # pfiVisitId
  COMBINED=1
  CENTROID=0
Communications to the other system
  Input to Gen2
    R.A. and Dec. of a field center (case2)
  Output
    R.A. and Dec. corresponding to actual telescope position (case1)
TBC
  Field center will be pointed by SetupField command
  What number should be the default for EXPTIME
  Command format of AGCC actor?
  Whether IIC or AGCC the command should be sent?
#**********************************************************************
#
# AG camera exposure
# sending a command to AGCC
#
#**********************************************************************
:Header
SCRIPT_AUTHOR=Moritani, Koshida
SCRIPT_UPDATE=2021.10.05
OBE_ID=PFS
OBE_MODE=SPEC_ENG
:Parameter
#for PFS
SSYS=PFI
NFRAME=1
EXPTIME=1
#DOCENTROID=FALSE
# Object (passed to Gen2 FITS.PFS.OBJECT status.)
OBJECT="test" # dark|test|object
PFIVISITID=0 # pfiVisitId
COMBINED=1
CENTROID=0
:Command
:start
# Calc timelimit for sequence of exposure
*SET TIMELIM = $EXPTIME + 15
*SET TIMELIM_TOT = (30 + $TIMELIM * $NFRAME)
:main_start
*SET INFO2="$NFRAME x $EXPTIME sec"
EXEC OBS Set_Message Instrument_name=PFS obsinfo1="AG Camera exposure" obsinfo2= obsinfo2=$INFO2 obsinfo3=clear obsinfo4=clear obsinfo5=clear ;
*FOR $NFRAME COUNT IN
*SET INFO3="$COUNT / $NFRAME frame"
EXEC OBS Set_message Instrument_name=PFS obsinfo3=$INFO3;
EXEC OBS SOUND SELECT=E_EXPSTART Volume=64 ,
EXEC PFS PFSCMD ACTOR="agcc" CMD="expose $OBJECT pfsVisitId=$PFIVISITID exptime=$EXPTIME combined=$COMBINED centroid=$CENTROID" TIMELIM=$TIMELIM ;
EXEC OBS SOUND SELECT=E_EXPDONE Volume=64 ;
*ENDFOR
## Sound : file is in /gen2/conf/Sounds/
#EXEC OBS SOUND SELECT=PFS_CRITICALALERT Volume=64 ,
EXEC OBS Set_Message Instrument_name=PFS obsinfo3="Done" ;
:main_end
:end

## Slide 31: Function ID 4: Agexp.sk
Operational sequence
  [Gen2] Display a message to Gen2 window
    “AG camera exposure starting” (EXEC OBS SET_MESSAGE)
  [Gen2] Send exposure command to AGCC actor.
    “expose” command
    Input parameters:
  [AGCC] Take exposure and store the images
    Return values: image file path (broadcasted to MHS status key-value pairs)
    Images will be stored in ICS storage server
  [Gen2] Display a message to Gen2 window
    “AG camera exposure done” (EXEC OBS SET_MESSAGE)
Discussion
  Should M2 position recorded in opDB and FITS header?

## Slide 32: Function ID 5: PFS_AGFOCUS.sk
Run the focusing sequence on AG actor
Functions:
  Run focusing sequence with AG cameras
  “focus” command of AG actor
Header
  SCRIPT_AUTHOR=Moritani, Koshida
  SCRIPT_UPDATE=2021.09.21
  OBE_ID=PFS
  OBE_MODE=SPEC_ENG
Default parameters
  EXPTIME=1
  Z=!TSCL.Z
  ADJ_Z="FALSE" # TRUE | FALSE
  OBJECT="FOCUSING"
Note
  Kawanomoto-san is developing core focusing software which calculate the focus error and tilt?
  Target should be obtained from opDB?
  Focus command format for AG actor
#**********************************************************************
#
# AG camera focusing sequence
# sending a command to IIC and AG actor
# performs focusing sequence at the current telescope pointing
#
#**********************************************************************
:Header
SCRIPT_AUTHOR=Moritani, Koshida
SCRIPT_UPDATE=2021.09.21
OBE_ID=PFS
OBE_MODE=SPEC_ENG
:Parameter
#for PFS
EXPTIME=1
Z=!TSCL.Z
ADJ_Z="FALSE" # TRUE | FALSE
# Object (passed to Gen2 FITS.PFS.OBJECT status.)
OBJECT="FOCUSING"
:Command
:start
# Calc timelimit for sequence of exposure
*SET TIMELIM = (15 + ($EXPTIME + 5))
:main_start
EXEC OBS Set_Message Instrument_name=PFS obsinfo1="Focusing (AG actor)" obsinfo2=clear obsinfo3="Start" obsinfo4=clear obsinfo5=clear ,
*Set $EXPT_AG = $EXPTIME * 1000
exec pfs pfscmd actor="ag" cmd="focus expTime=$EXPT_AG" ;
EXEC OBS Set_Message Instrument_name=PFS obsinfo3="Done. " obsinfo4="Focus offset: " obsinfo5=!FOCUS_OFFSET ;
# Adjust focus position
*IF "$ADJ_Z" == "TRUE"
EXEC OBS Set_Message Instrument_name=PFS obsinfo2="Adjusting focus to" obsinfo3=($Z + !FOCUS_OFFSET) obsinfo4=clear obsinfo5=clear ,
EXEC TSC TELFOCUS COORD=ABS F_SELECT=P_OPT2 Z=($Z + !FOCUS_OFFSET) ;
EXEC OBS SOUND SELECT=COMMAND_COMPLETE Volume=64 ,
EXEC OBS Set_Message Instrument_name=PFS obsinfo2="Done." obsinfo3="z=" obsinfo4=!TSCL.Z obsinfo5=($Z + !FOCUS_OFFSET);
*ENDIF
:main_end
:end

## Slide 33: Function ID 5: AGFocus.sk
Operational sequence
  [Gen2] Display a message to Gen2 window
    “AG focus starting” (EXEC OBS SET_MESSAGE)
  [Gen2] Register target information to opDB… Optional?
  [Gen2] Pointing telescope
    [Gen2] Convert R.A. and Dec. into Az El
    [TSC] Rotate the insrot to the input position
    [Gen2] Display a message “Slewing Telescope”
    [TSC] Drive the telescope to the target position
    [Gen2] Display a message “Waiting for Rotator/Focus/WindScreen to Settle”
    [Gen2] Check status and wait for the InsRot settled
  AG actor sequence (from Yoshida-san’s manual ss 4.3)
    [Gen2] Execute the focus command with target identifier and exposure time
    [AG, AGCC] Take an exposure with specified exposure time.
    [AGCC] Store centroids and other statistics of detected stellar objects in opDB.
    [AG] Retrieve centroids and other statistics of detected stellar objects from opDB.
    [AG] Compute focus error and tilt of the focal plane.
    [AG] Set the FOCUS_OFFSET Gen2 status.
    [Gen2] Adjust the focus position in response to FOCUS_OFFSET (EXEC TSC TELFOCUS COORD=ABS F_SELECT=P_OPT2 Z=(!TSCL.Z + !FOCUS_OFFSET)).
  [Gen2] Display a message to Gen2 window
    “AG focus done” (EXEC OBS SET_MESSAGE)

## Slide 34: Function ID 6: PFS_STARTAG.sk
Initializing and run AG sequence. Function to execute Acquire_field either from pfsDesign or from actual pointing of the telescope should be implemented.
Functions:
  Field acquisition
Header
  OBE_ID=PFS
  OBE_mode=ENG
  COMMAND=SETUPFIELD
  Script_Version=1.0
  Script_Author=PFS
  Script Update=2021/??/??
Default parameters
  EXPTIME=1
  AG="ON"
  DESIGN_PATH=NOP # /export/home/pfs/pfsDesign-0x0000000000000001.fits
  INTERVAL=10
  DESIGN_ID=1
  VISIT_ID=0
Note
<Header>
OBE_ID=HSC
OBE_mode=IMAG
COMMAND=SETUPFIELD
Script_Version=0.3
Script_Author=Nakata/Tait/Utsumi
### This script is created based on SETUPFILED.sk of SupCam.
Script_Update=2013.02.02
Script_Update=2014.07.04
# Dispatcher_Version=1.0
# ESTIMATE=180
</Header>
<Default_Parameter>
DATASET_ID=DS000
RA=!STATS.RA
DEC=!STATS.DEC
EQUINOX=!STATS.EQUINOX
INSROT_PA=!TSCL.INSROTPA_PF
OFFSET_RA=0
OFFSET_DEC=0
OBJECT=DUMMY
Z=!TSCL.Z
FILTER=NOP
FILE=NOP
</Default_Parameter>
<Command>
:START
:MAIN_START
{
#
# AG off
#
EXEC TSC AG_TRACKING MOTOR=OFF ;
*Set INFO3="Target : $OBJECT"
Exec OBS Set_Message Instrument_Name=HSC ObsInfo1="SetupField : No Guiding / No Dithering" ObsInfo2=Clear ObsInfo3=$INFO3 ObsInfo4=Clear ObsInfo5=Clear ,
#
# calculate pointing
#
*IF "$FILE" == "NOP"
EXEC OBS CONVSECRADEC RASEC=$OFFSET_RA DECSEC=$OFFSET_DEC RABASE=$RA DECBASE=$DEC ;
EXEC OBS CALC_RADEC MODE=PLUS RABASE=$RA DECBASE=$DEC RAOFFSET=!STATOBS.RARELOUT DECOFFSET=!STATOBS.DECRELOUT ;
EXEC TSC INSROT_PF TELESCOPE=LINK COORD=ABS POSITION=$INSROT_PA ;
EXEC TSC TELDRIVE COORD=ABS RA=!STATOBS.RACALCOUT DEC=!STATOBS.DECCALCOUT EQUINOX=$EQUINOX ,
Exec OBS Set_Message Instrument_Name=HSC ObsInfo2="Slewing Telescope" ,
*ELSE
EXEC TSC INSROT_PF TELESCOPE=LINK COORD=ABS POSITION=$INSROT_PA ;
Exec OBS Set_Message Instrument_Name=HSC ObsInfo2="Slewing Telescope" ObsInfo4="Non Sidereal Tracking" ,
EXEC TSC TELDRIVE COORD=FILE TARGET=$FILE DIRECTION=TSC ;
EXEC OBS CONVSECRADEC RASEC=$OFFSET_RA DECSEC=$OFFSET_DEC RABASE=!STATS.RA DECBASE=!STATS.DEC ;
Exec TSC TELDRIVE_Offset COORD=ABS RA=!STATOBS.RARELOUT DEC=!STATOBS.DECRELOUT ;
*ENDIF
Exec TSC TelFocus Motor=on Coord=TSC F_Select=P_OPT2 Z=$Z ;
};
#
# chceck status
#
Exec OBS Set_Message Instrument_Name=HSC ObsInfo2="Waiting for Rotator/Focus/WindScreen to Settle" ,
Exec OBS Check_Status Mode=AND Timeout=0360 N1=[STATS.ROTDIF_PF -0.005 +0.005] ;
Exec OBS Check_Status Mode=AND Timeout=0030 N1=[STATL.ZDIF -0.005 0.005] ;
# Exec OBS Check_Status Mode=AND Timeout=0720 N1=[STATL.WINDSDIF -10.0 +0.5] ;
Exec OBS Check_Status Mode=AND Timeout=0720 N1=[STATL.WINDSDIF_SIGN -0.5 +10.0] ;
Exec OBS Set_Message Instrument_Name=HSC ObsInfo2="Done" ;
#
:MAIN_END
:END
</Command>

## Slide 35: Function ID 6: PFS_STARTAG.sk
Operational sequence
  [Gen2] Display a message to Gen2 window saying “M2 Setup starting” (EXEC OBS SET_MESSAGE)
  [TSC] Send M2_SETUP command to TSC with parameters.
    If “FOCI” is set to “NOP”, the explicitly specified values for each axes are used. Otherwise, TSC will set the Hexapod position to PFS nominal position.
  [Gen2] Display a message to Gen2 window saying “M2 Setup done” (EXEC OBS SET_MESSAGE)

## Slide 36: Function ID 7: AGON.sk, AGOFF.sk, AGRECONF.sk
Halt/Resume/Reconfigure AG sequence.
AGON.sk
Functions:
  Resume the previously running AG sequence
Header
  SCRIPT_AUTHOR=Moritani, Koshida
  SCRIPT_UPDATE=2021.09.22
  OBE_ID=PFS
  OBE_MODE=SPEC_ENG
Default parameters
  EXPTIME=1
  DESIGN_ID=1
  DESIGN_PATH="/export/home/pfs"
  FROM_VISIT_ID=0
  SKY="yes"
Note
#**********************************************************************
#
# Start AG sequence at the current position
# sending a command to AG actor
#
#**********************************************************************
:Header
SCRIPT_AUTHOR=Moritani, Koshida
SCRIPT_UPDATE=2021.09.22
OBE_ID=PFS
OBE_MODE=SPEC_ENG
:Parameter
#for PFS
EXPTIME=1
DESIGN_ID=1
DESIGN_PATH="/export/home/pfs"
FROM_VISIT_ID=0
SKY="yes"
:Command
:start
:main_start
EXEC OBS Set_Message Instrument_name=PFS obsinfo1="AGon" obsinfo2=clear obsinfo3="Start" obsinfo4=clear obsinfo5=clear ;
exec pfs pfscmd actor="ag" cmd="autoguide start design_id=$DESIGN_ID design_path=$DESIGN_PATH from_visit_id=$FROM_VISIT_ID sky=$SKY" ;
# oneCmd.py ag autoguide start design_id=1 design_path=/export/home/pfs from_visit_id=0 sky=yes
EXEC OBS Set_Message Instrument_name=PFS obsinfo3="Done. " ;
:main_end
:end

## Slide 37: Function ID 7: AGON.sk, AGOFF.sk, AGRECONF.sk
AGOFF.sk
Functions:
  Halt the currently running AG sequence
  Change the exposure time of AG cameras
Header
  SCRIPT_AUTHOR=Moritani, Koshida
  SCRIPT_UPDATE=2021.09.22
  OBE_ID=PFS
  OBE_MODE=SPEC_ENG
Default parameters
  None
Note
#**********************************************************************
#
# Stop running AG sequence
# sending a command to AG actor
#
#**********************************************************************
:Header
SCRIPT_AUTHOR=Moritani, Koshida
SCRIPT_UPDATE=2021.09.22
OBE_ID=PFS
OBE_MODE=SPEC_ENG
:Parameter
:Command
:start
:main_start
EXEC OBS Set_Message Instrument_name=PFS obsinfo1="AGoff" obsinfo2=clear obsinfo3="Start" obsinfo4=clear obsinfo5=clear ;
#exec pfs pfscmd actor="ag" cmd="autoguide start"
exec pfs pfscmd actor="ag" cmd="autoguide stop" ;
EXEC OBS Set_Message Instrument_name=PFS obsinfo3="Done. " ;
:main_end
:end

## Slide 38: Function ID 7: AGON.sk, AGOFF.sk, AGRECONF.sk
AGRECONF.sk
Functions:
  Change the exposure time of AG cameras
Header
  SCRIPT_AUTHOR=Moritani, Koshida
  SCRIPT_UPDATE=2021.09.22
  OBE_ID=PFS
  OBE_MODE=SPEC_ENG
Default parameters
  EXPTIME=NOP
  INTERVAL=NOP
Note
#**********************************************************************
#
# Stop running AG sequence
# sending a command to AG actor
#
#**********************************************************************
:Header
SCRIPT_AUTHOR=Moritani, Koshida
SCRIPT_UPDATE=2021.09.22
OBE_ID=PFS
OBE_MODE=SPEC_ENG
:Parameter
EXPTIME=NOP
INTERVAL=NOP
:Command
:start
:main_start
*IF "$EXPTIME" == "NOP"
*ELSE
*Set $EXPT_AG = $EXPTIME * 1000
*IF "$INTERVAL" == "NOP"
*ELSE
*Set $INT_AG = $INTERVAL * 1000
EXEC OBS Set_Message Instrument_name=PFS obsinfo1="AG Reconfigure" obsinfo2=clear obsinfo3="Start" obsinfo4=clear obsinfo5=clear ;
#exec pfs pfscmd actor="ag" cmd="autoguide start"
exec pfs pfscmd actor="ag" cmd="autoguide reconfigure exposure_time=$EXPT_AG cadence=$INT_AG"
EXEC OBS Set_Message Instrument_name=PFS obsinfo3="Done. " ;
:main_end
:end

## Slide 39: Function ID 7: AGON.sk, AGOFF.sk, AGRECONF.sk
Operational sequence
  [Gen2] Display a message to Gen2 window saying “M2 Setup starting” (EXEC OBS SET_MESSAGE)
  [TSC] Send M2_SETUP command to TSC with parameters.
    If “FOCI” is set to “NOP”, the explicitly specified values for each axes are used. Otherwise, TSC will set the Hexapod position to PFS nominal position.
  [Gen2] Display a message to Gen2 window saying “M2 Setup done” (EXEC OBS SET_MESSAGE)

## Slide 40: Function ID 8: PFS_MCS_MULTI_EXP2.sk
Take MCS images
Functions:
  Take MCS images setting number of images taken, exposure time, object name in FITS header
Header
  SCRIPT_AUTHOR=Yabe, Moritani
  SCRIPT_UPDATE=2019.08.15
  OBE_ID=PFS
  OBE_MODE=SPEC_ENG
Default parameters
  SSYS=MCS
  NFRAME=2
  EXPTIME=1
  EXPTYPE=OBJECT
  DOCENTROID=FALSE
  EL=!STATS.EL
  ROTA=!STATS.IROTPF_POS
  DEL=0
  DROTA=0
  NMOVE_EL=1
  NMOVE_ROTA=1
  OBJECT=nop
TBC
  Current pointing position is taken from Gen2 status (MLP1?)
  Is it really that simple?
  Syntax for AG on/off command in AG actor
#**********************************************************************
#
# MCS multiple exposure 2 (M-4, P-4)
#
# -- Interleave telescopemove(El, Rot) and exposure
#
#**********************************************************************
:Header
SCRIPT_AUTHOR=Yabe, Moritani
SCRIPT_UPDATE=2019.08.15
OBE_ID=PFS
OBE_MODE=SPEC_ENG
:Parameter
# for PFS
SSYS=MCS
##Exposure
NFRAME=2
EXPTIME=1
EXPTYPE=OBJECT
DOCENTROID=FALSE
# Telescope movement
EL=!STATS.EL
ROTA=!STATS.IROTPF_POS
DEL=0
DROTA=0
NMOVE_EL=1
NMOVE_ROTA=1
# Object (passed to Gen2 FITS.PFS.OBJECT status.)
OBJECT=nop
:Command
:start
# set counters
asn cntel = 0
asn cntrt = 0
# For nesting to rotation move without el move
*IF ($DEL) == (0)
asn totel = 1
*ELSE
asn totel = ($NMOVE_EL)
*ENDIF
# Move telescope to initial position and take exposure
EXEC TSC AzElDrive COORD=abs AZ=NOP EL=$EL ,
EXEC TSC InsRot_PF Telescope=free COORD=abs POSITION=$ROTA ;
#*SUB PFS_POPT2_MOVE OBE_ID=PFS OBE_MODE=ENG COMP=ADC MMODE=EL EL=$EL TELESCOPE=free ;
# Forth argument IN is mandatory
# The third argument is needed even if not used.
#*FOR $NFRAME NF IN
# EXEC PFS MCSEXPOSE EXPTYPE=$EXPTYPE EXPTIME=$EXPTIME DoCentroid=$DOCENTROID;
#*ENDFOR
# Sound : file is in /gen2/conf/Sounds/
EXEC OBS SOUND SELECT=E_EXPSTART Volume=64 ,
*FOR $NFRAME COUNT IN
*SET INFO3="$COUNT / $NFRAME frame"
EXEC OBS Set_message Instrument_name=PFS obsinfo1=clear obsinfo2=clear obsinfo3=$INFO3 obsinfo4=clear obsinfo5=clear ;
EXEC PFS MCSEXPOSE EXPTYPE=$EXPTYPE EXPTIME=$EXPTIME DoCentroid=$DOCENTROID ;
*ENDFOR
#asn count = 0
#while(@count < $NFRAME){
# asn count = @count + 1
# EXEC OBS Set_message Instrument_name=PFS obsinfo1=clear obsinfo2=clear obsinfo3="@count / $NFRAME frame" obsinfo4=clear obsinfo5=clear;
# EXEC PFS MCSEXPOSE EXPTYPE=$EXPTYPE EXPTIME=$EXPTIME DoCentroid=$DOCENTROID;
#}

## Slide 41
Operational sequence
:main_start
# Move telescope step by step
while ((@cntel) < (@totel)) {
asn cntel = @cntel + 1
EXEC TSC AzElDrive COORD=rel AZ=0 EL=$DEL ;
asn nel=($EL + $DEL * (@cntel+1))
# *SUB PFS_POPT2_MOVE OBE_ID=PFS OBE_MODE=ENG COMP=ADC MMOVE=EL EL=@nel TELESCOPE=free;
while(@cntrt < $NMOVE_ROTA){
asn cntrt = (@cntrt + 1)
EXEC TSC InsRot_PF Telescope=free COORD=rel POSITION=$DROTA ;
*FOR $NFRAME COUNT IN
*SET INFO3="$COUNT / $NFRAME frame"
EXEC OBS Set_message Instrument_name=PFS obsinfo1=clear obsinfo2=clear obsinfo3=$INFO3 obsinfo4=clear obsinfo5=clear ;
EXEC PFS MCSEXPOSE EXPTYPE=$EXPTYPE EXPTIME=$EXPTIME DoCentroid=$DOCENTROID ;
*ENDFOR
# asn count = 0
# while(@count < $NFRAME){
# asn count = @count + 1
# EXEC OBS Set_message Instrument_name=PFS obsinfo1=clear obsinfo2=clear obsinfo3="@count / $NFRAME frame" obsinfo4=clear obsinfo5=clear;
# EXEC PFS MCSEXPOSE EXPTYPE=$EXPTYPE EXPTIME=$EXPTIME DoCentroid=$DOCENTROID;
# }
}
}
:main_end
EXEC OBS SOUND SELECT=E_EXPDONE Volume=64 ;
:end
Function ID 8: PFS_MCS_MULTI_EXP2.sk

## Slide 42: Function ID 9: PFS_FIBRE_LIGHT.sk
Fiber illuminator control
Functions:
  Turn on/off the fiber illuminator through PFI Ebox
Header
  SCRIPT_AUTHOR=Moritani
  SCRIPT_UPDATE=2021.09.18
  OBE_ID=PFS
  OBE_MODE=SPEC_ENG
Default parameters
  SSYS=SPS
  FF=on
  FF_POWER=35
  FF_PERIOD=100
  SF=on
  SF_POWER=65
Note
#**********************************************************************
#
# SpS Command : Abort
#
#**********************************************************************
:Header
SCRIPT_AUTHOR=Moritani
SCRIPT_UPDATE=2021.09.18
OBE_ID=PFS
OBE_MODE=SPEC_ENG
:Parameter
# for PFS
SSYS=SPS
FF=on
FF_POWER=35
FF_PERIOD=100
SF=on
SF_POWER=65
:Command
:start
# Nothing to execute here
:main_start
EXEC OBS Set_message obsinfo1=clear obsinfo2="Illuminators" obsinfo3="FF $FF" obsinfo4="SF $SF" ;
## Fiducical Fiber
if $FF == "ON"
EXEC PFS PFSCMD ACTOR="peb" cmd="led config ledperiod=$FF_PERIOD dutycycle=$FF_POWER" ;
EXEC PFS PFSCMD ACTOR="peb" cmd="led off" ;
EXEC PFS PFSCMD ACTOR="peb" cmd="led on" ;
elif $FF == "OFF"
EXEC PFS PFSCMD ACTOR="peb" cmd="led off" ;
else
EXEC OBS Set_message obsinfo3="No option for $FF";
endif
## Science Fiber
if $SF == "ON"
EXEC PFS PFSCMD ACTOR="sps" cmd="bia on power=$SF_POWER" ;
elif $SF == "OFF"
EXEC PFS PFSCMD ACTOR="sps" cmd="bia off" ;
else
EXEC OBS Set_message obsinfo4="No option for $SF";
endif
EXEC OBS Set_message obsinfo5="Done" ;
:main_end
# Nothing to execute here
:end

## Slide 43: Function ID 9: PFS_FIBRE_LIGHT.sk
Operational sequence

## Slide 44: Function ID 10: PFS_SPS_EXPOSURE.sk
Take an exposure of SpS
Functions:
  Take an exposure of SpS
  Set number of images taken, exposure time, obgect information in FITS header, camera used, calibration lamp
Header
  SCRIPT_AUTHOR=Moritani
  SCRIPT_UPDATE=2019.08.27
  OBE_ID=PFS
  OBE_MODE=SPEC_ENG
Default parameters
  SSYS=SPS
  NFRAME=1
  EXPTIME=1
  EXPTYPE=OBJECT
  CAMERA="b1,r1"
  HGAR=1.0
  AR=1.0
  NE=1.0
  KR=1.0
  HAL=1.0
  SEQ_HEAD=noseq
  SEQ_TAIL=noseq
  SEQ_NAME="viaGen2"
  SEQ_COMMENT="fromGen2"
  OBJECT=nop
Note
  Always used with SetupField command
  Collect status of SpS (disperser, calib lamp, etc.)
#**********************************************************************
#
# SpS Basic Exposure command
# executing doBias, doDark and doExposure
#
#**********************************************************************
:Header
SCRIPT_AUTHOR=Moritani
SCRIPT_UPDATE=2019.08.27
OBE_ID=PFS
## Overwrite Gen2 FITS.PFS.OBS-MOD status
OBE_MODE=SPEC_ENG
:Parameter
#for PFS
SSYS=SPS
## Sps uses "duplicate" as the number of frames
NFRAME=1
EXPTIME=1
EXPTYPE=OBJECT
## Which camera to be used
CAMERA="b1,r1"
## Default value of on-time [sec] for each cal-lamp source
HGAR=1.0
AR=1.0
NE=1.0
KR=1.0
HAL=1.0
## command before/after exposure
SEQ_HEAD=noseq
SEQ_TAIL=noseq
SEQ_NAME="viaGen2"
SEQ_COMMENT="fromGen2"
# Telescope
# Object (passed to Gen2 FITS.PFS.OBJECT status.)
OBJECT=nop
# TIMELIM=30
:Command
:start
# Calc timelimit for sequence of exposure
*SET TIMELIM = (30 + ($EXPTIME + 30) * $NFRAME)
# Common Parameters about camera
*sps_set = "cam=$CAMERA name=$SEQ_NAME comment=$SEQ_COMMENT"
:main_start
EXEC OBS Set_Message Instrument_name=PFS obsinfo1=clear obsinfo2="SpS exposure: $NFRAME X $EXPTIME sec" obsinfo3="See Monitor tab" obsinfo4=clear obsinfo5=clear ;
# Sound : file is in /gen2/conf/Sounds/
EXEC OBS SOUND SELECT=E_EXPSTART Volume=64 ,
if $EXPTIPE == "bias"
EXEC PFS PFSCMD ACTOR="iic" CMD='bias duplicate=$NFRAME $sps_set' TIMELIM=$TIMELIM;
elif $EXPTIPE == "dark"
EXEC PFS PFSCMD ACTOR="iic" CMD='dark expTime=$EXPTIME duplicate=$NFRAME $sps_set' TIMELIM=$TIMELIM;
elif $EXPTIPE == "arc"
EXEC PFS PFSCMD ACTOR="iic" CMD='scienceArc hgar=$HGAR argon=$AR neon=$NE krypton=$KR $sps_set' TIMELIM=$TIMELIM;
elif $EXPTIPE == "trace"
EXEC PFS PFSCMD ACTOR="iic" CMD='scienceTrace halogen=$HAL $sps_set' TIMELIM=$TIMELIM;
else
EXEC OBS Set_Message Instrument_name=PFS obsinfo4="Sorry. No option for $EXPTIPE" obsinfo5=clear ;
endif
#EXEC OBS SOUND SELECT=E_EXPDONE Volume=64 ,
EXEC OBS SOUND SELECT=PFS_CRITICALALERT Volume=64 ,
EXEC OBS Set_Message Instrument_name=PFS obsinfo3="Done" ;
:main_end
:end

## Slide 45: Function ID 10: PFS_SPS_EXPOSURE.sk
Operational sequence